## Slide 1: 6 Figure Grid References

## Slide 2: Ordnance Survey Maps
The horizontal lines that run across a map are called northings - they increase in value as they go up the map from the bottom.
The vertical lines that run across a map are called eastings - they increase in value as they go across the map from left to right.

## Slide 3: 4 – figure grid references
It is straightforward to find a specific place using a grid reference.
Grid references are easy if you can remember that you always have to go along the corridor before you go up the stairs.
- To find the number of a square first use the eastings to go along the corridor until you come to the bottom left-hand corner of the square you want. Write this two-figure number down. - Then use the northing to go up the stairs until you find the same corner. Put this two‑figure number after your first one and you now have the four-figure grid reference.

## Slide 4: 6 Figure Grid References
Finding a 6 figure grid reference
Sometimes you want to find the location of something more accurately than a whole square.
You have to imagine that that one box identified in a four figure grid reference is broken down into smaller squares – 10 x 10 squares, which are marked all around the edges of your map. (see next slide)
Starting with “0” as the number of the first box – count across from the Easting line to where you are and add this to your Easting number of your four figure grid reference.
Then you do the same with the Northing – starting with “0” in the first box – count up how many squares you are from the bottom northing line of the square.
Putting these together you have your six figure grid reference.

## Slide 5
21
22
37 0
38
A
A= 21,37
= 214,376
= 210,373
0 1 2 3 4 5 6 7 8 9 0
0
1
2
3
4
5
6
8
9

## Slide 6
12
13
14
34
35
36
A
B
A= 136 ,354
B= 122,343

## Slide 7: 6 Figure Grid References Exercise
= __ __ __ , __ __ __
= __ __ __ , __ __ __
= __ __ __ , __ __ __
= __ __ __ , __ __ __
= __ __ __ , __ __ __
= __ __ __ , __ __ __
12
11
10
09
08
41
42
43
44
45

## Slide 8: Exercise Answers
= 416,104
= 448,119
= 443,087
= 428,112
= 422,092
= 435,100